## Slide 1: Measurements Workflow

## Slide 2: Overview
Switch
Background traffic
(Replay real traffic)
Probes
(Generate low-rate traffic to sample end-to-end latency)
Server A
LatPerf
TcpReplay
NIC
NIC
NFV
Infrastructure
(DUT)
NIC
Notes: 我们用的是XL710网卡，该网卡的固件系统版本需要降级。

## Slide 3: Steps
Wire the device as mentioned in last ppt
Setup command in switch
  ssh to switch, run setup scripts
    init_bridge.sh, vnfProfileRules.sh
Setup for NFVI
  Run pytest on Server A
    SelfAdaptiveMano/sam/serverController/vnfController/test/profiling/test_fwProfiling.py
Start measurement
  Run autoProfiler’s main scrips
    latPerf/autoProfiler/main.py

## Slide 4: NFVI Type
Software SFF
BESS as Software SFF
Physical SFF
P4 as Physical SFF
Software SFF
Switch
Switch
(Physical SFF)
Intel NIC
Intel NIC
Enable SR-IOV
Please focus on this type
We will focus on this type later

## Slide 5: Measure without switch
目前的测量系统比较繁琐，需要一个switch来中转流量。我们需要一个更简单的测量方案，即用一个网卡完成时延测量，如下图：
Background traffic
(Replay real traffic)
Probes
(Generate low-rate traffic
to sample end-to-end latency)
Server A
MoonGen
NIC
NFV
Infrastructure
(DUT)
NIC

## Slide 6: TODO Tasks
实现单网卡测量工具：
  方案一：使用MoonGen（推荐这种方案）
    Moongen是一个开源的流量生成工具，它能够重放真实流量，但是它是否支持同时测量出时延是一个还未确定的事情，需要进一步调研，下面是一些MoonGen的lua脚本：
      https://github.com/emmericp/MoonGen/blob/master/examples/pcap/replay-pcap.lua
      https://github.com/emmericp/MoonGen/blob/master/examples/l3-load-latency.lua
      https://github.com/emmericp/MoonGen/blob/master/rfc2544/benchmarks/latency.lua
    建议在虚拟机环境中验证（调整网卡的驱动为e1000，该驱动支持DPDK）：
      一台作为Server A，另一台虚机作为DUT
      Server A运行Moongen，DUT运行NFVI（sam）
      Moongen生成IP-IN-IP的probe流量以及pcap的重放流量
    MoonGen对XL710网卡固件版本和驱动有特殊要求，需要更新固件版本和驱动，否则吞吐量只有16Mpps(64B packet)。
      固件版本：firmware 5.04
        https://github.com/emmericp/MoonGen/issues/211
Notes: 性能有瓶颈XL710网卡最多到16Mpps
MoonGen
sudo ./build/MoonGen /home/smith/HaoChen/Projects/SLOMO_DEBUG/traffic_generator/traffic_generation.lua 0 0 --dpdk-config=./libmoon/dpdk-conf-targetNF.lua
sudo ./build/MoonGen /home/smith/HaoChen/Projects/SLOMO_DEBUG/traffic_generator/traffic_generation.lua 0 0 --dpdk-config=./libmoon/dpdk-conf-comp1.lua
多流量生成进程
https://github.com/emmericp/MoonGen/issues/163
Scaling issues with multiple cores and ports
https://github.com/emmericp/MoonGen/issues/230

## Slide 7: TODO Tasks
实现单网卡测量工具：
  方案二：基于DPDK开发测量工具（如果MoonGen不行，再用这个方案）
    可以参考pktgen等工具源码开发
    开发量应该小于等于latPerf代码的2倍

## Slide 8: Measure latency of each SFC Instance (flow)
目前的测量系统只能测出一条SFCI的端到端时延，如果要测量N个SFCI，则需要串行地测量，例如下图，需要先测量橙色的SFCI，再测量黄色的SFCI。目前autoProfilier没有实现这部分串行测量的代码。
Background traffic
(Replay real traffic)
Probes
(Generate low-rate traffic
to sample end-to-end latency)
Server A
MoonGen
NIC
NFV
Infrastructure
(DUT)
NIC
Software SFF

## Slide 9: TODO Tasks
实现这部分的代码来测量多SFCI情景下（即存在性能干扰时）的每条SFCI的端到端时延。